## OpenHUDware.car

## This open source design outlines a DIY electric vehicle. The design is loosely based on quad coptor drones with 4 independent motors removing the need for a traditional drivetrain. The control system is also electronic as in drones, removing the need for a mechanical steering column.
## The design is intended as a platform to run OpenHUD software, using an LCD screen as a replacement for the traditional windscreen. Basically because I’ve wanted cars to have HUDs since I was a kid. Realistically these are two completely seperate projects and you could put an LCD on any old car, or have a DIY electric car without it.
## Ardupilot-rover open source software is used as the backbone of the control system.
## Additional work could be done to integrate google maps navigation with something like missionplanner or QgroundStation to make the car follow a predefined route.
## OpenHUD has object detection capabilities, but the neural networks used in OpenHUD would need additional training before full self-driving capabilities could be used.
## Design alternatives
- build a basic frame from scratch without any trim or comfort features. Allows independent suspension and steering. Allows zero turn. finished cost (estimated) ~$10,000.
## get an old car for like $500 (+~$2500 for motors and batteries) and gut it. Small car weighs around 1300kg, removing the motor and un-needed components should bring it down close enough to 1000kg.
## Design Power
As a basis for comparison the Mini Cooper S has a power to weight ratio of 100W/kg. The least powerful Tesla has a motor power of around 200kw. Assuming around half of this power for a first time build
100kW (4x25kW motors) = 1000kg @ 100W/kg (e.g. 100W/kg)
work per wheel
1000kg/4 wheels = 250kg
r=0.241m
T= F * d
35 = m*a*d	(motor torque is 35Nm per motor see below)
35 =250*0.241*a
a=0.58m/s/s

v=ut+0.5at^2
60(/3.6)=0+0.5*0.5*t^2
t=8.12
0-60km/h in approx 8.5 seconds
## Design weights and cost

## STEERING, DRIVE AND SUSPENSION

Independant suspension at each wheel.

Mc Pherson Struts
Tie / sway

A linear actuator is used at each wheel to push/pull the wheel around its vertical axis in order to steer. This allows each wheel to steer independantly.

Motor

EXPANDED VIEW

Linear Actuator for steering

CV axle

Steering Tie

## A Motor is attached to each wheel, connected by a CV axel. This allows each wheel to spin independantly without requiring a diff, and also allows wheels to spin in opposite directions, allowing zero turn functionality.
## Motors
MOTOR: MP-120100
MAX VOLT: 100V
MAX POWER: 22000W-25000W
MAX DRAW: 220-250A
ESC: ~250A
Rated power:12kw
Sustained draw: 120A @ 100V

SIZE: 120 x 120 ( without shaft )
Stator: 60mm
WEIGHT (g): 3.935
SHAFT: 12mm
MAX TORQUE: 35Nm (tesla roadster produces maximum torque of 270 N⋅m, Almost double the torque per wheel, which makes sense – it also has double the total power at around 50kw/wheel)
https://www.alibaba.com/product-detail/40hp-25KW-Outrunner-Electric-Motorcycle-Paraglider_60468056520.html?spm=a2700.wholesale.0.0.190e61e8YvrVye

## Battery
Nissan leaf has 40kwh @350V =150Ah
Tesla Roadster 53kWh = 320km
Roadster uses 13.5 kWh/100km
Battery Capacity of 13.5-15kW should provide about 100km range.
15kWh/100V = 150Ah
This requires 7 of the following batteries in series.
https://www.alibaba.com/product-detail/CATL-4S1P-14-8V-150Ah-NMC_1600543065321.html?spm=a2700.galleryofferlist.normal_offer.d_title.1d8459b2kz6k64

## SEATS
https://www.alibaba.com/product-detail/Black-Fiber-Glass-for-Universal-Automobile_60786999946.html?spm=a2700.galleryofferlist.0.0.13a816fckn73oM

## Linear Actuators

Model	FD1
Input voltage	12V/24V/110V DC
Load capacity	Max 6000N (push) / 4000N (pull)
Speed	4 ~ 40mm/s (no load)
Stroke	26mm ~ 1000mm (Customized Stroke Available)
Duty cycle	10%
Limit switches	Built-in, factory preset
Operation temperature	-20°C~ +40°C
Noise decibel	≤48 dB
Protection class	IP44
Minimum installation distance	≥stroke+160mm

https://www.alibaba.com/product-detail/12V-24V-electric-linear-actuator_317110836.html?spm=a2700.galleryofferlist.topad_classic.d_title.148f1ba8zJ4gv2

## CV Axels 150
https://www.alibaba.com/product-detail/EPX-Front-left-Axle-Driving-Shaft_1600380300483.html?spm=a2700.wholesale.0.0.f2636e101nnIAB
## Frame & Materials (TO BE REDESIGNED)
Base = 2m x 3m
Roof = 2m x 3m
Sides = 3m x 1.5m
Ends = 1.5m x 2m
(20 x 20 x 1.6mm) Galvanised Square Hollow Section

See Spreadsheet.