The internal registers and memory of the MPU-9250 can be accessed using either I2C at 400 kHz or SPI at 1MHz. SPI operates in four-wire mode. For
applications requiring faster communications, the sensor and interrupt registers may be read using SPI at 20MHz. Due the to importance of low latency gyro signals, SPI was chosen.

https://invensense.tdk.com/wp-content/uploads/2015/02/PS-MPU-9250A-01-v1.1.pdf

To prevent switching into I2C mode when using SPI, the I2C interface should be disabled by setting the I2C_IF_DIS configuration bit. Setting this bit should be performed immediately after waiting for the time specified by the “Start-Up Time for Register Read/Write” in Section 6.3. For further information regarding the I2C_IF_DIS bit, please refer to the MPU-9250 Register Map and Register
Descriptions document.

[4]	Serial Clock output (SCLK),
[5]	Serial Data Output (SDO)
[6]	Serial Data Input (SDI)
[7]	Chip Select (CS)

https://github.com/kriswiner/MPU6050/wiki/Affordable-9-DoF-Sensor-Fusion
In 2010 Sebastian Madgwick developed simple 6 DoF IMU and 9 DoF MARG (Magnetic, Angular Rate, Gravity) sensor fusion algorithms optimized for high filter update rates on small microcontrollers. They are capable of matching the performance of the proprietary filters in the Invensense DMP in terms of accuracy and filter update rates, and allow full 9 DoF sensor fusion that the DMP cannot do as of yet.

#include "MPU9250.h"

// an MPU9250 object with the MPU-9250 sensor on SPI bus 0 and chip select pin 10
MPU9250 IMU(SPI,10);
int status;

void setup() {
  // serial to display data
  Serial.begin(115200);
  while(!Serial) {}

  // start communication with IMU
  status = IMU.begin();
  if (status < 0) {
    Serial.println("IMU initialization unsuccessful");
    Serial.println("Check IMU wiring or try cycling power");
    Serial.print("Status: ");
    Serial.println(status);
    while(1) {}
  }
  // setting DLPF bandwidth to 20 Hz
  IMU.setDlpfBandwidth(MPU9250::DLPF_BANDWIDTH_20HZ);
  // setting SRD to 19 for a 50 Hz update rate
  IMU.setSrd(19);
  // enabling the data ready interrupt
  IMU.enableDataReadyInterrupt();
  // attaching the interrupt to microcontroller pin 1
  pinMode(1,INPUT);
  attachInterrupt(1,getIMU,RISING);
}

void loop() {}

void getIMU(){
  // read the sensor
  IMU.readSensor();
  // display the data
  Serial.print(IMU.getAccelX_mss(),6);
  Serial.print("\t");
  Serial.print(IMU.getAccelY_mss(),6);
  Serial.print("\t");
  Serial.print(IMU.getAccelZ_mss(),6);
  Serial.print("\t");
  Serial.print(IMU.getGyroX_rads(),6);
  Serial.print("\t");
  Serial.print(IMU.getGyroY_rads(),6);
  Serial.print("\t");
  Serial.print(IMU.getGyroZ_rads(),6);
  Serial.print("\t");
  Serial.print(IMU.getMagX_uT(),6);
  Serial.print("\t");
  Serial.print(IMU.getMagY_uT(),6);
  Serial.print("\t");
  Serial.print(IMU.getMagZ_uT(),6);
  Serial.print("\t");
  Serial.println(IMU.getTemperature_C(),6);
}

https://electropeak.com/learn/interfacing-mpu9250-spi-i2c-9-axis-gyro-accelerator-magnetometer-module-with-arduino/